## Slide 1: Model-based Engineering for Quadcopter Control Software
Vrushank Agrawal
Advisor: Timothy bourke
Co-Advisor: Basile Pesin

## Slide 2: Introduction
  Quadcopter
    Unmanned Aerial Vehicle and a type of drone
    Embedded System which uses
      RTOS
      parallelism
      works with time constraints
2

## Slide 3: Quadcopter Movement
  6 Degrees of Freedom (DOF)
  4 State Variables
    Thrust
    Roll
    Pitch
    Yaw
3

## Slide 4: Crazyflie system design
4
  A combination of tasks that run parallelly on the microcontroller
  Led sequence for setting the leds
  Feedback control loop
    Takes sensors’ input
    Gives controlled input to the hardware

## Slide 5: FreeRTOS Scheduler
  FreeRTOS
  Task states in FreeRTOS
  Preemptive scheduler
  Idle Task
5

## Slide 6: Problem
  Quadcopters written in C/C++ from initial state diagrams
  Hard to understand the code and model and test system behavior
6

## Slide 7
Alternative Approach
  Write the code in a Dataflow Synchronous Language like Heptagon
  Inspired from Lustre and offers modern features like delays, automata, switch
7

## Slide 8
Our Goal
  Write parts of the Crazyflie source code (written in C) in Heptagon
  The thesis is in continuation with CSE303 project which was dedicated to understanding the Crazyflie source code
  PID controller already implemented by colleagues, so, integrate and test the integration in Crazyflie.
  Implement state estimation, led sequence task, and Kalman task in Heptagon
8

## Slide 9: Cascaded PID Controller Dataflow diagram
9

## Slide 10: Merging Heptagon-generated C code
    For every node, Heptagon generates two data types:
        mem - contains reference to the current state
        out - contains output of node.
10
    And two types of functions :
        reset – initializes temporary variables used in the node
        step – evaluates code of the Heptagon node

## Slide 11: Complementary Filter Dataflow diagram
11

## Slide 12: Complementary Filter Debugging
    Debug testing environment
12
Bug in Heptagon compiler
Fast inverse square root and Floating-point numbers

## Slide 13: Led Seq Dataflow diagram
13
    Final output
    Internal timers
State machines

## Slide 14: Led sequence FreeRTOS task analysis
14
    Possible task running time can vary as show in the diagram
Timing aspect analysis

## Slide 15: Extended Kalman Filter
15
    Rearranging code
Issues with stack pointer debugged using disassembly

## Slide 16: Conclusion
Results
Parts of feedback control loop and FreeRTOS tasks (led sequence) were successfully implemented as Heptagon nodes
Dataflow diagrams from Heptagon can be used to generate the low-level C code
Further Steps
Extended Kalman Filter can be debugged and integrated in the firmware.
Other FreeRTOS tasks including the High-Level Commander can be integrated as Heptagon nodes.
16

## Slide 17: Thank You